## Slide 1
Secure IoT / Edge Network
Utilizing Zero-Trust Architecture
CE313 — Computer Communications & Networks
Ali Muntazir 2023098
Abubakar Butt 2023352
Ismail 2023453
Usman 2023581
GIK Institute of Engineering Sciences & Technology

## Slide 2
THE PROBLEM
Why traditional campus networks fail in the IoT era
Implicit Trust by Default
The moment a device is plugged into the LAN, it is trusted — regardless of whether it's a managed workstation or a cheap factory sensor with default credentials.
Weak Device Security
Temperature probes, IP cameras & smart locks ship with weak credentials, no firmware update path, and outdated TLS stacks. Yet they sit on the same network as critical systems.
Castle-and-Moat Is Broken
A compromised HVAC controller gives attackers the same lateral reach as a fully patched workstation. The perimeter has been easy to breach for over a decade.
Industry 4.0 reality: 50+ heterogeneous IoT endpoints on one factory floor — most unpatched, some unmanageable.

## Slide 3
Zero-Trust
Architecture
NIST SP 800-207
"
Never trust,
always verify.
01
Explicit Verification
Authenticate & authorise every packet, every host, every user — regardless of network location.
02
Least-Privilege Access
Grant minimum permissions needed. Micro-segment the network into 8 VLANs so a sensor can only talk to its gateway.
03
Assume Breach
Design controls so that the failure of ANY ONE does not collapse the whole. Five independent layers, each at a different OSI layer.

## Slide 4
NETWORK ARCHITECTURE
Three-tier hierarchical topology for a 15,000 m² smart-manufacturing plant
PERIMETER
pfSense / Cisco ASA (FW-01)
CORE
ISR 4451 (CR-01) · Catalyst 9300 (CS-01)
DISTRIBUTION
Catalyst 3850 × 2 — Redundant, DAI
ACCESS
Catalyst 2960 × 3 — Office · Production · Servers
WIRELESS / EDGE
Aironet 4800 (802.11ax) · RPi 4 Edge Gateway
10.50.0.0/16 supernet — 8 VLANs
OM4 fibre 10G core links
Max 3 switching hops: Access → WAN
Rapid-PVST+ loop prevention

## Slide 5
VLAN MICRO-SEGMENTATION
VLAN 10
MGMT
10.50.10.0/24
Switch & router management
VLAN 20
SERVERS
10.50.20.0/24
RADIUS · Syslog · NTP
VLAN 30
OFFICE
10.50.30.0/23
Corporate workstations
VLAN 40
PRODUCTION
10.50.40.0/24
OT workstations & HMIs
VLAN 50
IOT_SENSORS
10.50.50.0/23
General-purpose IoT (50+ ep)
VLAN 60
IOT_CRITICAL
10.50.60.0/24
Safety locks · Alarms
VLAN 70
GUEST
10.50.70.0/24
Internet-only visitors
VLAN 80
VPN_REMOTE
10.50.80.0/24
WireGuard / IPsec pool
Native VLAN 999 on all trunks — defence against double-tagging VLAN-hopping attacks

## Slide 6
IoT EDGE GATEWAY
Bringing intelligence to the building boundary
200 ms
Cloud-anchored latency
Before edge gateway
15 ms
Edge decision latency
92.5% reduction
82 GB
Daily WAN egress (raw)
Without filtering
8.2 GB
Daily WAN egress
After batching (9× less)
How the Edge Gateway Works
1
Local Rule Evaluation
Threshold-crossing events trigger control responses (e.g. closing a safety relay) entirely on-site.
2
Temporal Aggregation
Raw samples are batched & decimated before forwarding north — 10× data reduction.
3
Topic-Based Filtering
Non-actionable MQTT messages are dropped at the Mosquitto broker before hitting the WAN.
Stack: Mosquitto MQTT (TLS/8883) + Node-RED on Raspberry Pi 4

## Slide 7
ZERO-TRUST SECURITY STACK
Five independent controls — each at a different OSI layer
5
Encrypted Tunnels
WireGuard / IPsec
Transport / Network
4
Perimeter Firewall
pfSense / Cisco ASA
Network
3
Dynamic ARP Inspection
DAI + DHCP Snooping
Data Link
2
Port Authentication
IEEE 802.1X / MAB (RADIUS)
Data Link
1
VLAN Micro-Segmentation
8 VLANs, native VLAN 999
Data Link
Compromise of any one layer does NOT collapse the others.

## Slide 8
VPN COMPARISON: WireGuard vs. IPsec
Chart: Throughput (Mbps) on 1 Gbps Link
| Cleartext | WireGuard | IPsec (IKEv2/AES-GCM)
Throughput (Mbps) | 942 | 847 | 623
10%
WireGuard overhead
vs 34% for IPsec
12 ms
WireGuard RTT
IPsec: 28 ms
~4K
WireGuard codebase
lines vs 100K+ IPsec
Fixed
Cipher suite
No negotiation surface
Verdict: WireGuard is the primary VPN for this deployment. IPsec retained only for legacy site-to-site partners.

## Slide 9
TCP CONGESTION CONTROL: Reno vs. BBR
Under 5% emulated wireless packet loss — Linux iPerf3 testbed
324 Mbps
TCP Reno
1,247 retransmissions
568 Mbps
TCP BBR
342 retransmissions
+75%
Throughput gain
BBR over Reno
−73%
Retransmissions
Fewer with BBR
Why does this matter for a factory?
TCP Reno's flaw: Treats every packet loss as congestion — halves the send window. On wireless links where loss is mostly corruption (not congestion), this is exactly the wrong response.
TCP BBR's approach: Models the bottleneck bandwidth and round-trip propagation delay directly, then paces against that model — ignoring the loss signal. Results: 75% more goodput, 73% fewer retransmissions.
Deployment recommendation: Set BBR as the default congestion algorithm (sysctl net.ipv4.tcp_congestion_control=bbr) on all Linux hosts in the factory network.

## Slide 10
HTTP/3 OVER QUIC
Future-proofing IoT telemetry transport
+92%
Throughput vs HTTP/2
−60%
Time-to-First-Byte
Runs over UDP — no TCP head-of-line blocking
0-RTT resumption: sensor reconnects instantly after radio outage
Multi-stream: loss on one telemetry stream doesn't stall others
TLS 1.3 mandatory — encrypted by design
92% gain validated vs nginx HTTP/2 under same 5% loss profile
Implementation
Library
aioquic (Python)
Port
UDP/4433
TLS
1.3 (mandatory)
Response
JSON telemetry
Host
Linux (real testbed)
Note: Packet Tracer only simulates HTTP/1.1 — all HTTP/3 figures from Linux testbed.

## Slide 11
PERFORMANCE RESULTS
Packet Tracer simulation + Linux iPerf3 testbed
Chart: End-to-End RTT to WAN (ms)
| PC0 (wired) | PC1 (wired) | Server1 | Server3 (same VLAN) | Tablet PC0 (Wi-Fi) | Tablet PC2 (Wi-Fi)
Mean RTT (ms) | 4 | 3 | 5 | 0 | 20 | 20
4 ms
Wired mean RTT
20 ms
Wireless mean RTT
5×
Wireless latency penalty (CSMA/CA)
3 hops
Core → Access path (TTL verified)
First-packet 25% loss on all hosts is expected ARP cache population — not a defect.
Management VLAN (VLAN 10) ping failed to WAN — correct Zero-Trust segmentation behaviour.

## Slide 12
CONCLUSION
What we built. What we measured. What we learned.
What We Built
Three-tier campus network (Cisco IOS)
Eight VLAN micro-segments
Zero-Trust: 802.1X + DAI + FW + VPN
Edge gateway: MQTT + Node-RED
HTTP/3 telemetry endpoint
Key Results
4 ms wired RTT · 20 ms wireless
WireGuard: 10% overhead vs 34% IPsec
BBR: +75% throughput vs Reno
Edge: 200 ms → 15 ms decision latency
HTTP/3: +92% throughput vs HTTP/2
Lessons Learned
Segment on day 1 — not after an incident
Wireless 5× penalty is structural (CSMA/CA)
Hybrid workflow: Packet Tracer + Linux
ZTA must be multi-vendor in production
Edge computing pays off at WAN scale
GIK Institute · CE313 Computer Communications & Networks · 2025